## Slide 1: Arduino Workshop
By
Devansh Srivastava
ISRO Intern, hG Joint Secretary, IEEE SB Chairman

## Slide 2: What is Arduino?
A company manufacturing open-source micro-controllers.
Some of the famous boards are Arduino Uno R3, Arduino NANO, Arduino MEGA, Arduino Leonardo etc.

## Slide 3: What is Micro-controller?
A computer on chip.
Components of Micro-controllers-
1- Micro-processor
2- Input/Output Interfacing Ports
3- Communication Channels
4- Memory(RAM/ROM)
5- Power pins/plugs

## Slide 5: Features of Arduino UNO R3

## Slide 6: Overview
Processor- ATmega 328P
14 digital i/o pins and 6 analog i/o pins
16MHz ceramic resonator
USB jack, AC-to-DC power adapter and Power Pins
Supports Arduino IDE for programming.

## Slide 7: Technical Specs
Operating Voltage- 5V (input voltage can be 6V-20V)
DC current per I/O pin- 20mA
Flash Memory- 32kB
SRAM- 2kB
EEPROM- 1kB

## Slide 8: Embedded System Hardware Architecture
Embedded System Hardware Architecture

## Slide 9: Sensors
Used to read the stimulus of the environment
Analogous to eye/ear/tongue/skin of the Human body
Some of the popularly used sensors are-
1- Ultraviolet Sensor
2- Infrared Sensor, PIR Sensor
3- Axis Sensor, Gyroscope, Accelerometer
4- Flex Sensor

## Slide 10: Actuators
Used to perform the action that we want the ES to do
Analogous to hand/leg/throat of the human body
Some of the widely used actuators are-
1- DC,AC and Stepper Motors
2- LED and LCD Module
3- Speaker

## Slide 11: Arduino Programming

## Slide 12
Arduino Programming is very similar to C. All the rules of C is applicable in Arduino IDE.
IDE editor has two inbuilt functions- void setup() and void loop()
void setup() is used to configure the input/output ports and initialize the Terminal Window generally.
void loop() contains the main body of the code that has to run for infinite times

## Slide 13: Some inbuilt functions
digitalWrite( pinnumber, ACTION )- used to produce digital outputs at any output port. ACTION can be either HIGH or LOW
digitalRead(pinnumber)- used to intake digital inputs at any input port
Serial.begin(‘baudrate’)- initializes the terminal window
Serial.println(“message”)- prints and change the line in terminal window
delay(‘time in milliseconds’)- produces delay of given amount
pinMode(pinnumber, Mode)- defines the character of pin

## Slide 14: Some inbuilt functions
analogRead( pinnumber )- used to intake analog inputs at any analog port. In Arduino UNO, there is a 10-bit Analog to Digital Converter that maps 0-5V to 0-1023 value.
analogWrite(pinnumber, value)- used to output analog outputs at any analog port. Value lies in the range 0-255 depending on the duty cycle of PWM output.

## Slide 15: Blinking a LED

## Slide 16: Light LED using Potentiometer and Arduino

## Slide 17: QnA